The Program of comparative tests of the experimental "Type 1" spark plugs on A-76 gasoline and standard spark plugs on A-92 gasoline

- Base for the experimental test

- Engine MeMZ-245 (compression ratio 9,5)

- Stand with electrobalance machine, frequency range of the shaft rotation 1000 – 4500 min-1

- Initial tuning parameters of the engine MeMZ-245 has been corresponded to the specifications of the manufacturer.

- Engine behavior:

- Outside speed characteristic

- Test outcomes treatment

- Comparative estimation of engine processing parameters (Ne, M, ge, α) with experimental spark plugs "Type 1" on A-76 gasoline and standard spark plugs on A-92 gasoline

Outcomes of the experimental data have been presented in the tables 1-3 and on the picture 1. Outside speed characteristic has been covering regimes exploitation zone of engine MeMZ-245 on the increased loads. Detonation combustion of air-fuel mixture is expected to be appeared in the regimes exploitation zone of engine MeMZ-245 on the increased loads. Motor fuel is A-76 and A-92 gasoline.  Air parameters at the test moment are +27-30 ˚С temperature and 750-751 mm Hg pressure.

Parameters of engine work on the A-76 gasoline with “Type 1” spark plugs and base regulation of engine are following:

- The twisting moment of the engine is rising on 1,2 Nm

- The power is rising on 0,4 kW

- The specific effective expense of fuel decreases (to 10g/kWh)

- Engine working process without detonation is possible only at frequency of rotation of a crankshaft  n>2900 min-1

Engine work without detonation on the all regimes have been completed through  implementation of the later corner of an advancing ignition (5˚deg. crank angle after TDC) and work on the A-76 gasoline. The following parameters have been changed:

- Insignificant decrease of the twisting moment of the engine (on 0,7 Nm)

- Insignificant decrease of power (on 0,3 kW)

- The specific effective expense of fuel rises on 10g/kWh

In using standard spark plugs (А 17 ДВ) and A-76 gasoline detonation combustion starts with load 10-15% less then loads of outside speed characteristic regimes on A-76 gasoline both with fix corner of an advancing of ignition 5˚deg. crank angle after TDC and later corner of ignition (5˚deg. crank angle after TDC).

Table 1 – standard spark plugs А 17 ДВ, gasoline А-92, Өignition=5 ˚ before TDC

| № reg | n, min-1 | t cooling, ˚С | t exhaust gas, ˚С | СО | CnHm | Ne, kW | M, N*m | Ре, MPa | Gga, kg/h | ge, g/kWh | Gair, kg/h | α | ηv |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | 4020 |  |  |  |  |  |  |  |  |  |  |  |  |
|  | 4000 |  |  |  |  |  |  |  |  |  |  |  |  |
| 1 | 4010 | 83 | 600 | 2,1 | 200 | 28,8 | 68,73 | 0,792 | 8,633 | 299,05 | 124,818 | 0,977 | 0,825 |
|  | 3505 |  |  |  |  |  |  |  |  |  |  |  |  |
|  | 3510 |  |  |  |  |  |  |  |  |  |  |  |  |
| 2 | 3507,5 | 88 | 635 | 1,4 | 200 | 24,85 | 67,64 | 0,78 | 7,377 | 296,84 | 106,263 | 0,973 | 0,803 |
|  | 2985 |  |  |  |  |  |  |  |  |  |  |  |  |
|  | 2985 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 2985 | 87 | 613 | 0,98 | 180 | 22,51 | 71,98 | 0,83 | 6,207 | 275,79 | 90,473 | 0,985 | 0,803 |
|  | 2525 |  |  |  |  |  |  |  |  |  |  |  |  |
|  | 2518 |  |  |  |  |  |  |  |  |  |  |  |  |
| 4 | 2521,5 | 87 | 570 | 2,23 | 240 | 19,47 | 73,71 | 0,85 | 5,806 | 298,23 | 77,911 | 0,907 | 0,819 |

Table 2 – experimental spark plugs “Type 1”, gasoline А-76, Өignition=5 ˚ before TDC

| № reg | n, min-1 | t cooling, ˚С | t exhaust gas, ˚С | СО | CnHm | Ne, kW | M, N*m | Ре, MPa | Gga, kg/h | ge, g/kWh | Gair, kg/h | α | ηv |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | 3950 |  |  |  |  |  |  |  |  |  |  |  |  |
|  | 3980 |  |  |  |  |  |  |  |  |  |  |  |  |
| 1 | 3965 | 84 | 602 | 1,85 | 40 | 28,54 | 68,73 | 0,792 | 8,49 | 297,45 | 122,17 | 0,972 | 0,811 |
|  | 3500 |  |  |  |  |  |  |  |  |  |  |  |  |
|  | 3500 |  |  |  |  |  |  |  |  |  |  |  |  |
| 2 | 3500 | 88 | 650 | 1,41 | 20 | 25,83 | 70,46 | 0,812 | 7,214 | 279,28 | 107,42 | 1,006 | 0,808 |
|  | 3015 |  |  |  |  |  |  |  |  |  |  |  |  |
|  | 3015 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3015 | 88 | 630 | 0,73 | 30 | 23,01 | 72,85 | 0,84 | 6,25 | 271,67 | 92,2 | 0,997 | 0,805 |

Table 3 – Experimental spark plugs “Type 1”, gasoline А-76, Өз=5 ˚after TDC

| № reg | n, min-1 | t cooling, ˚С | t exhaust gas, ˚С | СО | CnHm | Ne, kW | M, N*m | Ре, MPa | Gga, kg/h | ge, g/kWh | Gair, kg/h | α | ηv |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | 3975 |  |  |  |  |  |  |  |  |  |  |  |  |
|  | 3995 |  |  |  |  |  |  |  |  |  |  |  |  |
| 1 | 3985 | 88 | 673 | 2,04 | 110 | 27,96 | 66,99 | 0,772 | 8,612 | 307,98 | 124,62 | 0,978 | 0,821 |
|  | 3500 |  |  |  |  |  |  |  |  |  |  |  |  |
|  | 3500 |  |  |  |  |  |  |  |  |  |  |  |  |
| 2 | 3500 | 89 | 680 | 1,71 | 100 | 25,12 | 68,51 | 0,79 | 7,438 | 296,13 | 108,113 | 0,982 | 0,811 |
|  | 3020 |  |  |  |  |  |  |  |  |  |  |  |  |
|  | 3005 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | 3012,5 | 88 | 652 | 1,4 | 100 | 22,1 | 70,03 | 0,807 | 6,25 | 282,84 | 94,628 | 1,023 | 0,825 |
|  | 2500 |  |  |  |  |  |  |  |  |  |  |  |  |
|  | 2495 |  |  |  |  |  |  |  |  |  |  |  |  |
| 4 | 2497,5 | 88 | 580 | 5,6 | 170 | 19,31 | 73,82 | 0,851 | 6,218 | 321,95 | 79,515 | 0,864 | 0,836 |

Conclusions

- Experimental “Type 1" spark plugs manufactured by NPP “NEC” at Kharkiv have been making significant impact on combustion process, reduce intensity of detonation combustion at work on low octane gasoline.

- Parameters of engine work on the outside speed characteristic regimes are not changed, when base gasoline A-92 was changed to low octane gasoline A-76 with  experimental “Type 1" spark plugs  in the MeMZ-245 engine.

- Experimental “Type 1" spark plugs implementation in automobiles with MeMZ-245 engine allowing the lowering of octane number of using fuel to A-76. It will  cut the expenses on fuel for every 100km of automobile way.